## Slide 1: ACTUATORS
PREPARED BY,
S.BABITHA,AP,
IT,HITS.

## Slide 2: DEFINITION
Actuators are devices that convert control signals (usually electrical) into physical action (movement, heat, light, etc.).
In CPS, they bridge the gap between the cyber world and the physical world, enabling systems to influence their environment based on sensor inputs and computational decisions

## Slide 3: Role of Actuators in CPS
Receive commands from the processor/controller
Translate electrical signals into physical actions
Execute control decisions (e.g., turning a valve, moving a robot arm)

## Slide 4: Types of Actuators in CPS
Actuator Type | Function | Examples | CPS Applications
Electric Motors | Produce rotation or linear motion | DC motors, stepper motors, servo motors | Robotics, drones, vehicles
Solenoids | Create linear motion using electromagnetic force | Door locks, valves | Smart locks, fluid control
Hydraulic Actuators | Use fluid pressure to produce force/motion | Cylinders, motors | Heavy industrial machinery
Pneumatic Actuators | Use compressed air to drive motion | Air cylinders | Automation, manufacturing
Thermal Actuators | Generate heat or motion using temperature changes | Thermostats, shape memory alloys | HVAC, biomedical systems
Piezoelectric Actuators | Precise micro-movements via electric charge | Piezo motors | Precision positioning, optics
Light/LED Actuators | Emit light based on signals | LEDs, laser modules | Visual feedback, smart lighting
Sound Actuators | Generate sound or alerts | Buzzers, speakers | Alarms, voice notifications

## Slide 5: Example: Smart Home CPS Actuators
Device | Actuator Used | Function
Smart Door Lock | Solenoid | Lock/unlock the door remotely
Smart Thermostat | Thermal actuator | Regulate temperature
Smart Light | LED | Turn light on/off or change brightness
Smart Fan | Electric motor | Adjust fan speed

## Slide 6: Key Characteristics of Actuators
Precision: How accurately it performs the action
Speed: Response time to control signals
Power: Required electrical or mechanical power
Interface: PWM, analog, digital, or communication bus (I2C, CAN)
Durability: Depends on material and use case

## Slide 7: Control Flow Example in CPS
[Sensors] → [Processor/Controller] → [Actuators]
↑ Decision Logic ↓
Environment (Software) Physical Action