## Slide 1: AUTOMOTIVE ETHERNET IN CYBER-PHYSICAL SYSTEMS (CPS)
PREPARED BY,
S.BABITHA,AP,
IT,HITS.

## Slide 2: DEFN- AUTOMOTIVE ETHERNET
Automotive Ethernet is a high-speed, cost-effective, and scalable in-vehicle networking technology that has become a key enabler for modern automotive CPS like ADAS (Advanced Driver-Assistance Systems), infotainment, autonomous driving, and vehicle-to-everything (V2X) communication.
Automotive Ethernet is a customized version of standard Ethernet (IEEE 802.3) adapted for the automotive environment:
Operates reliably under harsh conditions (vibration, temperature, EMI)
Supports real-time and time-sensitive communication
Uses single-pair twisted cables to reduce weight and cost

## Slide 3: 🔑 Key Features
Feature | Description
High Bandwidth | Speeds from 100 Mbps to 10 Gbps (100BASE-T1, 1000BASE-T1, etc.)
Full-Duplex Communication | Simultaneous send/receive
Reduced Cabling | Single twisted-pair wiring (vs. traditional multi-wire harnesses)
Time-Sensitive Networking (TSN) | Ensures real-time, deterministic communication for safety-critical systems
Interoperability | Based on open IEEE standards
Power over Data Lines (PoDL) | Delivers power and data over a single pair

## Slide 4: Automotive Ethernet Architecture in CPS
Camera] ─┐
├───> [Switch] ───> [Central ECU] ───> [Cloud Gateway]
[LIDAR] ──┘ │
[Infotainment] ──────┘
End devices: Sensors (camera, radar, lidar), ECUs, infotainment
Ethernet Switches: Central nodes that manage and route data
Gateway ECU: Bridges between CAN/FlexRay/LIN and Ethernet networks

## Slide 5: Applications in Automotive CPS
System | Function
ADAS | Real-time sensor fusion from radar, lidar, cameras
Infotainment | High-speed video and audio streaming
Vehicle Diagnostics | OTA (over-the-air) updates and system health monitoring
Autonomous Driving | Connects AI compute units, sensor data, and actuators
V2X Communication | Enables vehicle-to-vehicle/infrastructure data exchange

## Slide 6: 🔄 Comparison: CAN vs. Automotive Ethernet
Feature | CAN | Automotive Ethernet
Speed | Up to 1 Mbps | Up to 10 Gbps
Payload | 8 bytes | 1500+ bytes
Topology | Bus | Star/switch-based
Use | Control systems | Data-intensive systems (ADAS, infotainment)
Real-Time Support | Yes (via priority) | Yes (via TSN)

## Slide 7: Advantages of Automotive Ethernet
Scales easily with growing data demands
Reduces cable weight and cost
Supports both safety-critical and high-bandwidth functions
Standardized and interoperable

## Slide 8: Challenges
Requires EMI shielding and robust connectors
Complex integration with legacy networks (CAN, LIN, FlexRay)
New diagnostic and security considerations