## Slide 1: CAN (CONTROLLER AREA NETWORK) IN CYBER-PHYSICAL SYSTEMS (CPS)
PREPARED BY,
S.BABITHA,AP,
IT,HITS.

## Slide 2: DEFN
CAN is a robust, real-time, and reliable communication protocol designed for embedded control systems.
Originally developed by Bosch for automotive applications, CAN is now widely used in industrial CPS, robotics, medical devices, and automation systems.

## Slide 3: 🔑 Key Features of CAN
Feature | Description
Multi-Master Bus | Any node can initiate communication if the bus is free
Broadcast Communication | Messages are broadcast to all devices; receivers decide relevance
Message-Based Protocol | Communication is based on messages, not node addresses
Real-Time Support | Message priority via identifiers ensures time-critical data gets through first
Error Detection & Handling | Built-in CRC checks, automatic retransmission, error confinement
Deterministic | Ensures predictable communication for real-time control

## Slide 4: CAN Bus Physical and Data Link Layer
Medium: Twisted-pair cable (differential signaling)
Speed: Up to 1 Mbps (standard CAN); CAN FD supports higher speeds
Message Frame: Includes identifier, control, data (0–8 bytes for classic CAN), and CRC

## Slide 5: Typical CAN Network Architecture in CPS
[Node A] ---+
|
[Node B] ---+--- CAN Bus (Twisted Pair)
|
[Node C] ---+
Each node contains:
Microcontroller with built-in or external CAN controller
Transceiver for differential signaling

## Slide 6: Applications of CAN in CPS
CPS Domain | Application Examples
Automotive CPS | Engine control units (ECU), airbags, ABS, infotainment
Robotics | Real-time coordination between motor controllers and sensors
Industrial Automation | PLC communication, motor drives, factory floor devices
Medical CPS | Medical imaging, ventilators, infusion pumps
Aerospace | Avionics systems and flight control computers

## Slide 7: Advantages of CAN in CPS
Highly reliable and fault-tolerant
Real-time message prioritization
Low-cost cabling and hardware
Supports up to 8 bytes per message (CAN FD supports more)

## Slide 8: Limitations
Limited data payload (classic CAN: 8 bytes/message)
Not suitable for high-bandwidth multimedia data
Limited to short-range (typically < 40m at high speeds)

## Slide 9: 🔄 Variants of CAN
Variant | Description
CAN 2.0A/B | Standard/extended frame format (11/29-bit identifiers)
CAN FD (Flexible Data Rate) | Allows longer payloads (up to 64 bytes) and higher speed
CANopen / DeviceNet | Higher-layer protocols for industrial use, built on CAN