## Slide 1: CPS SOFTWARE STACK
PREPARED BY,
S.BABITHA,AP,
IT,HITS.

## Slide 2: CPS Software Stack (SW Stack)
🧠 In Cyber-Physical Systems (CPS), the software stack defines how various layers of software—from hardware interfaces to application logic—interact to manage both cyber (computing/control) and physical (sensor/actuator) components.

## Slide 3: Overview of the CPS Software Stack
+----------------------------+
| Application Layer |
+----------------------------+
| Middleware Layer |
+----------------------------+
| Operating System (RTOS) |
+----------------------------+
| Hardware Abstraction |
+----------------------------+
| Device Drivers / Firmware|
+----------------------------+
| Hardware (Sensors/Actuators, MCU, etc.) |
+----------------------------+

## Slide 4: 🔍 Layer-by-Layer Explanation
⚙️ Hardware Layer
Physical components: Sensors, actuators, microcontrollers, SoCs
Interfaces: GPIO, ADC/DAC, I2C, SPI, UART
2. 🔌 Device Drivers / Firmware
Interface code that directly communicates with hardware
Converts raw signals to usable data for upper layers
3. 🧾 Hardware Abstraction Layer (HAL)
Standardizes hardware access across different platforms
Enables portability and reusability
4. ⏱️ Operating System Layer (RTOS)
Real-Time Operating System (RTOS) like FreeRTOS, VxWorks, Zephyr
Handles:
  Task scheduling
  Interrupt management
  Inter-process communication
  Timing and real-time guarantees

## Slide 5: Layer-by-Layer Explanation
5. 🛠️ Middleware Layer
Communication frameworks (e.g., DDS, MQTT, ROS)
Data serialization, messaging, and network protocols
Security services (authentication, encryption)
Resource discovery and management
6. 📲 Application Layer
User-level logic and control algorithms
Decision-making, analytics, AI/ML models
Human-machine interface (HMI)
Cloud/edge communication (e.g., dashboards, APIs)

## Slide 6: Example: Smart Traffic CPS SW Stack
Layer | Components
Application | Traffic control algorithms, web dashboard
Middleware | DDS for sensor-car communication
RTOS | QNX or VxWorks on edge controller
HAL | Abstracts traffic light control logic
Drivers | Camera sensor drivers, GPIO drivers
Hardware | Cameras, actuators for lights, edge processor

## Slide 7: Key Software Stack Features in CPS
Modularity: Separation of concerns across layers
Portability: HAL and middleware enable cross-platform deployment
Real-Time Capability: Ensures timely response in critical systems
Scalability: From embedded nodes to cloud-based systems
Security: Encryption, authentication, secure updates