## Slide 1: SCHEDULING REAL-TIME CONTROL TASKS IN CPS
PREPARED BY.
S.BABITHA,AP,
IT,HITS.

## Slide 2: DEFN
In Cyber-Physical Systems (CPS), real-time scheduling ensures that control tasks (like sensor reading, decision-making, and actuator control) execute within strict timing constraints.
Failing to meet these deadlines can result in system instability or unsafe behavior — especially in automotive, aerospace, industrial, or medical CPS.

## Slide 3: Real-Time Task Basics
Concept | Description
Task | A unit of work (e.g., read sensor, compute PID control, update actuator)
Period (T) | Time between successive task releases
Deadline (D) | Time by which the task must complete
Execution Time (C) | Time taken to complete the task
Response Time | Time from task release to completion

## Slide 4: Types of Real-Time Tasks
Task Type | Description | Example
Hard Real-Time | Must meet deadlines every time | Airbag deployment, pacemaker pulse
Firm Real-Time | Missing a deadline degrades performance | Video frame processing in ADAS
Soft Real-Time | Occasional deadline misses are acceptable | Smart lighting control

## Slide 5: Common Real-Time Scheduling Algorithms
Algorithm | Type | Key Idea | Best Use
Rate Monotonic Scheduling (RMS) | Fixed-priority | Shorter period = higher priority | Periodic, static systems
Earliest Deadline First (EDF) | Dynamic-priority | Task with closest deadline first | High processor utilization
Deadline Monotonic | Fixed-priority | Deadline dictates priority | When deadlines < periods
Round Robin | Time-sharing | Equal time slices for all tasks | Non-critical soft real-time tasks
Priority-Based Preemptive | Fixed/dynamic | High-priority tasks can interrupt low-priority ones | Mixed criticality systems

## Slide 6: Example: Periodic Control Tasks Scheduling
Task | Period (T) | Execution Time (C) | Deadline (D) | Priority (RMS)
Sensor Reading | 10 ms | 1 ms | 10 ms | High
Control Logic (PID) | 20 ms | 2 ms | 20 ms | Medium
Data Logging | 100 ms | 5 ms | 100 ms | Low