## Slide 1: Processors in CPS Hardware Platforms
PREPARED BY,
S.BABITHA,AP,
IT,HITS

## Slide 2: DEFN
Processors are the core computational units in Cyber-Physical Systems (CPS).
They perform data acquisition, signal processing, control logic, and communication.
The choice of processor depends on the system's real-time needs, power constraints, and application complexity.

## Slide 3: Types of Processors Used in CPS
Type | Description | Use Cases
Microcontrollers (MCUs) | Low-power, single-chip processors with built-in I/O, timers, and memory | IoT devices, sensors, medical implants
Digital Signal Processors (DSPs) | Specialized for fast signal processing tasks (FFT, filtering, etc.) | Audio/video processing, motor control
System-on-Chip (SoC) | Combines CPU, GPU, memory, and peripherals on one chip | Smart cameras, drones, edge AI
Field-Programmable Gate Arrays (FPGAs) | Reconfigurable logic devices for parallel processing | High-speed control, image/video processing
Application-Specific Integrated Circuits (ASICs) | Custom-designed chips optimized for specific tasks | Pacemakers, industrial controllers
Multi-core Processors | Multiple cores allow parallel tasks | Smart cars, autonomous robots

## Slide 4: Processor Functions in CPS
Sensor Data Acquisition
  Read data from analog/digital sensors using ADC, I2C, SPI.
Real-Time Processing
  Apply filters, control algorithms (PID, AI-based), safety checks.
Decision Making & Actuation
  Translate control outputs into commands for actuators.
Communication
  Interface with wireless/wired networks (Wi-Fi, CAN, Zigbee).
Power & Resource Management
  Optimize energy usage, schedule tasks, manage peripherals.

## Slide 5: Examples of CPS Processors
Processor | Features | Example System
ARM Cortex-M Series | Low-power, real-time | Wearables, medical devices
Raspberry Pi (Broadcom SoC) | Linux-based, powerful | Smart home hubs, automation
Nvidia Jetson | GPU + CPU for AI | Drones, autonomous vehicles
TI C2000 DSP | Fast control loops | Power grid, industrial automation
Intel Atom | High-performance x86 | Industrial PCs, edge gateways