## Slide 1: SENSORS
PREPARED BY,
S.BABITHA,AP,
IT,HITS.

## Slide 2: DEFN
Sensors are critical hardware components in CPS that collect real-world data and convert it into electrical signals that processors can understand.
This enables perception, monitoring, and control in CPS environments.

## Slide 3: Classification of Sensors in CPS
Sensor Type | Measures | Examples | Applications
Temperature Sensors | Heat | LM35, DS18B20 | HVAC, smart agriculture
Pressure Sensors | Pressure/force | BMP180, MPX5010 | Automotive, aerospace
Motion Sensors | Movement/acceleration | Accelerometer (MPU6050), gyroscope | Wearables, robotics, drones
Proximity Sensors | Distance to objects | Ultrasonic, IR, LIDAR | Collision avoidance, automation
Light Sensors | Light intensity | LDR, TSL2561 | Smart lighting, agriculture
Gas/Chemical Sensors | Gas concentration | MQ series (MQ2, MQ135) | Environment monitoring, safety
Sound Sensors | Sound levels | Microphone modules | Voice control, security systems
Image Sensors | Visual data | CMOS/CCD camera modules | Surveillance, medical imaging
Position Sensors | Location/position | GPS, encoders | Smart vehicles, robotics
Touch Sensors | Physical touch/pressure | Capacitive sensors | Touch screens, wearables
Humidity Sensors | Moisture content | DHT11, DHT22 | Greenhouses, climate control

## Slide 4: Sensor Workflow in CPS
Physical Phenomenon → e.g., temperature, motion, sound
Sensor Measures It → converts to electrical signal
Signal Conditioning → filtering, amplification
Analog-to-Digital Conversion (ADC) → if needed
Processor Reads & Analyzes → control or report results
Actuators Respond or Data is Transmitted

## Slide 5: Example: Smart Healthcare CPS Sensors
Sensor | Role
ECG Sensor | Monitor heart activity
SpO2 Sensor | Measure blood oxygen level
Accelerometer | Detect falls or movement
Temperature Sensor | Monitor body temperature

## Slide 6: Integration Considerations
Sensor Accuracy & Precision
Power Consumption
Interface Type: Analog, I2C, SPI, UART
Sampling Rate: Real-time responsiveness
Calibration & Drift

## Slide 7
THANK YOU